## Slide 1
ME701
Docking Adapter
Latch Optimization
23B2120 | Aditya Nimbalkar

## Slide 2
OVERVIEW
0
  Problem Statement
03
  Notation
04
  Objective Function
06
07
-
-
-
-
  Optimizer
  Constraints
11
-
  Results
12
-

## Slide 3
PROBLEM STATEMENT
1
  The Docking Adapter Unit (DAU) uses a three-latch mechanism, each implemented as a planar RRRP linkage actuated by a linear slider.
  The slider motion produces a coupled radial and axial motion of the latch tip:
    Radial motion allows the latch to enter the recess of the female docking interface
    Axial motion pulls the two docking ports together and generates preload DAU-work-updates
  The geometry of this linkage determines the trajectory of the latch tip and the force transmission characteristics of the mechanism.
  A feasible linkage geometry has already been obtained through preliminary synthesis, but it is not optimal.

## Slide 4
NOTATION
2
H
dock,c

## Slide 5
NOTATION
2
a1
a2

## Slide 6
CONSTRAINTS
4
Radial Clearance: x_open >= R_hex
Interference Mitigation: x>= R_seat
Vertical Bounds: H_seat <= y_open <= H_dock,t
Latch Tip
Maximum Allowable Radial Footprint: a1 <= R_max - R
Hardware Interference: R - S >= 5mm
“Upward Bending Right Elbow”
Packaging
s
a1
a2
(R_seat,H_seat)
H_boss,c
H_boss,t
H_dock,c
H_dock,t
R_hex

## Slide 7
OBJECTIVE FUNCTION
4
  Closed Position Accuracy (Weight: 20): Heavily penalizes any deviation from the precise target seat coordinates (R_seat, H_seat) at the end of the stroke .
  Capture Capability (Weight: 15): Rewards designs that open wider than the required R_hex boundary, maximizing lateral capture margin .
  Axial Tolerance (Weight: 10): Rewards trajectories that maintain high clearance above the seat as the tip crosses the entry threshold, maximizing vertical misalignment tolerance .
PERFORMANCE TARGETS
s
a1
a2
(R_seat,H_seat)
H_boss,c
H_boss,t
H_dock,c
H_dock,t
R_hex

## Slide 8
OBJECTIVE FUNCTION
4
  Monotonic Motion (Weight: 15): Enforces strict inward and downward motion; heavily penalizes any trajectory that zig-zags or reverses direction to prevent jamming .
  Force Transmission (Weight: 8): Rewards high mechanical advantage. By favoring lower tip velocities porjected to downward motion, the mechanism guarantees higher pulling force when latching .
  Smoothness (Weight: 2): Minimizes trajectory acceleration (second derivative) to ensure smooth, predictable movement.
KINEMATIC METRICS
s
a1
a2
(R_seat,H_seat)
H_boss,c
H_boss,t
H_dock,c
H_dock,t
R_hex

## Slide 9
OBJECTIVE FUNCTION
4
Gradient-Friendly Walls (Weight: 50): Hard geometric and physical constraints are converted into smooth quadratic penalties
(e.g., max(0, “violation”)^2). This prevents the optimizer from getting "blinded" by abrupt mathematical cliffs .
  Plateau Problem with Discrete Penalties
SMOOTH PENALTIES
s
a1
a2
(R_seat,H_seat)
H_boss,c
H_boss,t
H_dock,c
H_dock,t
R_hex

## Slide 10
OBJECTIVE FUNCTION
4
20 * J_closed +
20 * J_capture +
10 * J_axial +
15 * J_mono +
2 * J_smooth +
8 * J_force +
50 * Penalty
OVERALL

## Slide 11
OPTIMIZER
4
  Gradient-Based
  SciPy Library
  Allows bounding variables
  Great for Constraint Non-Linear Optimization Problems
SLSQP (SEQUENTIAL LEAST SQUARES PROGRAMMING)

## Slide 12
RESULTS
4
OPTIMIZED MECHANISM PARAMETERS
Link 1 (a1) : 14.039 mm
Link 2 (a2) : 20.635 mm
Origin (R) : 25.000 mm
Slider Pos (s) : 20.000 mm
Coupler offset (u,v) : (38.372, -41.745) mm
KEY PERFORMANCE METRICS
Seat Target Error : 0.510 mm (dx: 0.366, dy: 0.355)
Lateral Capture Margin: 9.931 mm (Positive = correctly outside R_hex)
Open Tip Height : 66.964 mm (Constraint: < 80.0)
Axial Tolerance : 7.268 mm (Height margin above seat when passing R_hex)
Max Reach Required : 25.495 mm

## Slide 13
RESULTS
4
s
a1
a2
(R_seat,H_seat)
H_boss,c
H_boss,t
H_dock,c
H_dock,t
R_hex
OPTIMIZED MECHANISM PARAMETERS
Link 1 (a1) : 14.039 mm
Link 2 (a2) : 20.635 mm
Origin (R) : 25.000 mm
Slider Pos (s) : 20.000 mm
Coupler offset (u,v) : (38.372, -41.745) mm
KEY PERFORMANCE METRICS
Seat Target Error : 0.510 mm (dx: 0.366, dy: 0.355)
Lateral Capture Margin: 9.931 mm (Positive = correctly outside R_hex)
Open Tip Height : 66.964 mm (Constraint: < 80.0)
Axial Tolerance : 7.268 mm (Height margin above seat when passing R_hex)
Max Reach Required : 25.495 mm

## Slide 14
THANK YOU